## Slide 1: PinchPilot
Small hand movements for webcam desktop control
PRS Practice Module · First Project Presentation · Group 15
HE ZIHANG · WEI YI · CHI YONGJUN
6 October 2026

## Slide 2: What PinchPilot will do
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
A webcam can see a hand, but that does not make it a comfortable pointer. PinchPilot will let laptop users point, click, drag and scroll with small hand movements and finger pinches.
1
Show the hand
Clear in the preview, forearm resting on the desk
2
Pinch to move
Thumb and middle finger together; small hand or wrist motion
3
Click or drag
Index joins briefly: click. All three held: drag
4
Let go to pause
The pointer stays where it is; rest or reposition
re-grip to continue
An ordinary laptop webcam · macOS and Windows · used alongside the mouse or trackpad

## Slide 3: Why webcam pointing is hard to use today
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
A student is reading lecture notes on a laptop. They want to follow a link, scroll on and keep reading, without reaching for the mouse each time.
Reach for the mouse, again and again
Hand in the air: tiring and shaky
Goal: forearm supported, small pinch
With a webcam today | What goes wrong | Why
Moving the pointer across the screen | The arm gets tired | Large movements held in the air [1]
Making a small correction | The pointer shakes | Tracking jitter can be as large as the correction
Pinching to click | The click lands off target | The click gesture itself moves the hand
A gesture demo is not yet a daily tool: users must be able to correct, click, rest and resume without the pointer jumping.
[1] Hincapié-Ramos et al., Consumed Endurance: a metric to quantify arm fatigue of mid-air interactions, CHI 2014

## Slide 4: Project objectives
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
1
DESIGN
A low-effort interaction
Supported forearm and small movements; the pointer moves only while thumb and middle finger touch.
2
BUILD
A desktop tool
One application for macOS and Windows: preview, sensitivity, gesture switches, practice area and a stop control.
3
LEARN
Reliable contact recognition
Record our own gesture data and compare tuned rules, a random forest and a temporal CNN.
4
EVALUATE
Stability, errors and effort
Recognition on a person the model has never seen, then an internal usability pilot.
OUR MAIN QUESTION
Does learned contact recognition stay reliable when the hand is relaxed or turned, where fixed distance rules tend to fail?
Planned outputs: a working product and reproducible evidence from a small usability pilot.

## Slide 5: Related products and our focus
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
Existing option | What it offers | PinchPilot's focus
Mouse and trackpad | Familiar, direct desktop input | A complementary touch-free option for short tasks; the mouse stays available
Pawvis (macOS) | Webcam control with configurable and trained gestures | Explicit pinch roles, small hand and wrist motion, and support for macOS and Windows
MediaPipe hand tracking | A building block: 21 hand keypoints per frame | A usable interaction, a contact decision and a desktop experience built around the tracking
This is a positioning comparison. How well each option works will be established with matched user tasks; Pawvis is an optional product reference on the same Mac.

## Slide 6: Project scope
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
IN SCOPE
One control hand, the primary screen, short seated use
Point, click, double click, right click, drag, scroll, pause
An ordinary laptop webcam, on macOS and Windows
Camera frames are processed on the laptop
OUT OF SCOPE
Tracking the hand at every angle, or replacing the mouse
Retraining MediaPipe's hand-tracking model
Recruited participants: the three of us record the data
1
2
3
4
1
The hand being followed
2
The current action
3
Sensitivity and gestures
4
Stop control and Esc
Concept interface: a design drawing, not a screenshot

## Slide 7: Data required and available
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
What we need
REQUIRED
AVAILABLE NOW
Hand keypoints
From each camera frame
21 points
per frame
Yes
pretrained MediaPipe
Team recordings
Train and test contact models
3 people
3+ sessions, ~15 min
Not yet
starts 7 Oct
Unlabelled usage records
Pretraining; keypoints only
Keypoints
no video saved
Not yet
after recording starts
Synthetic examples
Software checks only
Checks
never results
Yes
generated
What each recording session will cover
GESTURES
Contact and release
Short taps
Grip plus click
Near-contact (no touch)
Hand adjustments
VARIED ON PURPOSE
Supported posture
Hand orientation
Distance
Lighting
Different days
Own laptop camera
Public gesture datasets such as HaGRID label static hand poses, not finger contact over time, so we record our own.
So we will test on a member whose recordings were never used for training, and report the limits of a three-person dataset.

## Slide 8: From recordings to training data
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
ONE MOMENT OF USE
HAND KEYPOINTS
FEATURES (SHORT SEQUENCE)
LABELS (THREE CONTACTS)
Laptop camera frames
About 30 per second
Processed locally
21 keypoints per frame
from pretrained MediaPipe, used as it is
Keypoints relative to the palm
Three fingertip distances
Time between frames
Thumb and middle
move
Thumb and index
click
Thumb and ring
right click
Contacts can be on together: a drag is the first two, held.
EXAMPLE The index tip moves to the thumb → the thumb–index distance falls over a few frames → thumb and index: touching
Labels prompts organise each trial · the team reviews every label · uncertain moments are marked, not guessed
Labels are never copied from the rules' own output; a second member checks a sample

## Slide 9: System design
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
Camera
Ordinary webcam; frames stay on the laptop
Hand keypoints
21 points per frame, pretrained MediaPipe
Where to point
Smoothing and sensitivity
Which fingers touch
Tuned rules or learned contact models
Interaction layer
Click
Drag
Scroll
Pause and release
Desktop
macOS and Windows mouse events
trained on team recordings with reviewed labels
One shared interaction layer
Recognisers can be swapped and compared without changing the gesture design.
Safe by default
One control hand will be locked; losing the hand will pause control and release held buttons.
Tools
Python, PySide6, MediaPipe, scikit-learn and PyTorch; one control engine for macOS and Windows.

## Slide 10: Pattern recognition techniques
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
SUPERVISED / UNSUPERVISED
Labels and reconstruction
Reviewed contact labels train the recognisers. An autoencoder learns features from unlabelled keypoint sequences.
MACHINE / DEEP LEARNING
Random forest and temporal CNN
Both read the same short keypoint sequence and output three contact decisions.
HYBRID / ENSEMBLE
Combined methods
A tree ensemble; pretraining followed by supervised fine-tuning; learned contact with rule-based interaction.
INTELLIGENT SENSING
From camera to action
Camera frames become hand keypoints, hand states, stable movement and desktop actions.
WHAT WE WILL COMPARE, ON THE SAME RECORDINGS
Tuned rules
the baseline and the fallback
Random forest
a classical learner
Temporal CNN
learns from the sequence
CNN + autoencoder pretraining
second priority
MediaPipe itself is not retrained. If learning adds little, tuned rules remain a valid fallback.

## Slide 11: How one click will be recognised
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
Worked example
1
Frames
The thumb and middle finger are together; the index finger moves to the thumb.
2
Keypoints
MediaPipe gives 21 keypoints per frame; the thumb–index distance shrinks.
3
Recogniser
Reads the last few frames and outputs three contact decisions.
4
Interaction
Touch, then release: a click at the held position. Held with the grip: a drag.
5
Desktop
The operating system receives an ordinary mouse click.
distance over time (sketch)
THUMB WITH
middle · touching
index · touching
ring · apart
short touch → click
all three held → drag
“The camera supplies keypoints, the recogniser decides which fingers touch, and the interaction layer turns that into a deliberate mouse action.”

## Slide 12: Evaluation plan
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
1
Contact recognition
Three-fold leave-one-person-out: test on a member never seen in training
Random forest and CNN against tuned rules, on the same recordings
Precision, recall, F1; missed and false events; latency
2
Pointer control
Basic position mapping against stabilised hand and wrist control
The same recogniser on both sides
Jitter, click displacement, re-grips and corrections
3
User value
Internal pilot: three members, three conditions, rotated order
Models trained without the tester's own recordings
Time, errors, effort, preference and NASA-TLX (a standard workload questionnaire)
Autoencoder pretraining (second priority): the same CNN with and without it, at 25%, 50% and all labels; results by hand orientation
The test member never guides training or tuning · settings are frozen before each test · three developer-testers give an internal pilot only

## Slide 13: Main risks and how we will handle them
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
1
RISK
Three people are a small dataset
HOW WE WILL HANDLE IT
Test on the member left out of training, report each person separately, and state person and camera effects as limits
2
RISK
Brief contacts are hard to label
HOW WE WILL HANDLE IT
Prompts organise the trials, uncertain moments are marked instead of guessed, and a second member checks a sample
3
RISK
Learning may not beat tuned rules
HOW WE WILL HANDLE IT
Tuned rules remain the fallback; if data collection slips, the autoencoder experiments are deferred first
Limits we will state: three developer-testers; one hand and one screen; MediaPipe's tracking errors are inherited.

## Slide 14: What we have done so far
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
1
1
Live hand tracking
2
2
State: grip engaged
3
3
Gesture switches
4
4
Practice and recording tools
Screen from our early prototype with the live camera. The interface text is in Chinese for now.
DONE
mostly design
✓
Interaction concept: supported forearm, small movements, pause and re-grip
✓
Gesture set (provisional): move, click, right click, drag, scroll, pause; tried in an early prototype
✓
Tools and methods chosen: MediaPipe keypoints; Python and PySide6; rules, random forest, temporal CNN
✓
Training and evaluation method designed: leave-one-person-out; checked on synthetic samples only
NOT YET
no accuracy numbers are claimed today
Team recordings: three members, at least three sessions each; recording starts on 7 October
Reviewed labels: the recording protocol is piloted first; a second member checks a sample
Model results on real data: tuned rules, random forest, temporal CNN; autoencoder second
Learned control and internal pilot: a learned recogniser in live use; three members, three conditions

## Slide 15: Work plan and next steps
1 Objectives · 2 Scope · 3 Data · 4 Technical approach · 5 Done so far
By 6 Oct
Demo and protocol
DONE WHEN
Basic desktop demo; pilot recording protocol
Demo reached
By 16 Oct
Control and data
DONE WHEN
Refined hand and wrist control; team recordings collected, labels reviewed
By 23 Oct
Models
DONE WHEN
Rules, random forest and CNN compared; configurations frozen
By 27 Oct
Internal pilot
DONE WHEN
Three members, three conditions; results per person
By 31 Oct
Deliverables
DONE WHEN
macOS and Windows builds, dataset, report, slides and video
We would welcome your feedback on the data plan and these priorities.

## Slide 16: AI tool declaration
OpenAI Codex and Anthropic Claude assisted with source research, proposal drafting, translation, review, figure design and document layout, and with preparing this presentation. The interface on slide 6 is a concept drawing; the screen on slide 14 is captured from our own early prototype, which was also developed with AI coding assistance.
The team is responsible for all content.

## Slide 17: Appendix A: evaluation details
Area | Baseline or comparison | Main measures
Contact recognition | Random forest and CNN against tuned geometric rules, on the same held-out recordings | Precision, recall, F1; missed and false events; unavailable input
Autoencoder pretraining | The same CNN with and without pretraining, at three label budgets | F1, missed and false events, latency; results by posture group
Pointer control | Basic mapping against stabilised hand and wrist control; same recogniser | Jitter, click displacement, movement, re-grips and corrections
User tasks | Basic rules; stabilised rules; stabilised control with learned recognition | Completion, time, errors, effort, NASA-TLX and preference
Product reference | Mouse or trackpad; optional Pawvis on the same Mac | Task performance and experience across products
Recognition: three-fold leave-one-person-out; pretraining uses only the training partition; settings are frozen before each test.

## Slide 18: Appendix B: proposed gestures
Function | Proposed gesture | Design purpose
Point | Hold thumb and middle finger together, then move the hand or wrist slightly | Small movements with deliberate control
Click and double click | Touch thumb and index finger, then release; repeat for a double click | Active clicks with less target displacement
Right click | Briefly pinch thumb and ring finger | A distinct action for context menus
Drag | Keep the thumb–middle grip and add the index to the thumb; after a short hold, move; release the index to drop | A familiar hold, move and release sequence
Scroll | Form a V with index and middle fingers and move slightly up or down | Read long pages while the pointer stays still
Pause and reposition | Release the thumb–middle grip, reposition and re-grip | Rest, or return inside the camera view